## Slide 1: HSRP-OSPF Network Resilience Project Final Project DEPI
Supervised by : Engineer Khaled Abd rabu

## Slide 2: Team members :
Menna Elgamel
Ahmed Abdslam
Fatma Elzhraa Adhem
Abanoub Mores
Hanaa Marzouk
Ahmed Emad

## Slide 3: Topology Diagram :

## Slide 4
Addressing Table

## Slide 5
Addressing Table
The lists interfaces, IP addresses, subnet masks, and gateways for:
Routers (R1 - R4)
Switch S1 (VLAN1 configuration)
Devices (D1, D2, D3)

## Slide 6: Learning Objectives:
Configure Device Basic Settings
Switch Security Configuration
Configure OSPF Dynamic Routing Protocol
Standard ACL configuration
2
3
4
5
1
6
Verify Network Connectivity
Document the configuration

## Slide 7: Scenario 01 02
configuring the routers to support IPv4 connectivity and LAN redundancy using HSRP.
configuring OSPF and verify connectivity. ​

## Slide 8: Router configuration
Setup
Interface

## Slide 9: PC and switch configuration: Assign IPs to PCs via Desktop Tab
D1:
172.40.180.10
255.255.255.0
D2:
172.41.180.10
255.255.255.128
D3:
180.20.180.10
255.255.255.192

## Slide 10: Switch Security Configuration:

## Slide 11: Testing the Switch Security
Add PCs: Connect two additional PCs (D4 and D5) to the hub.
IP Addresses: Assign D4 with 180.20.180.11 and D5 with 180.20.180.12 from the 180.20.180.0/26 network.
Ping Test:
Ping the R4 interface G0/0 (180.20.180.1) from D3, D4, and D5.
Verify MAC Addresses:
Use the show run command to check that MAC addresses are "sticking."

## Slide 13
OSPF Dynamic Routing Protocol Configuration
Step 1: Configure OSPF on R1
Configure OSPF on R1.
Advertise all directly connected networks in area 0 using classless network addresses.
Step 2: Configure OSPF on R2
Configure OSPF on R2.
Advertise all directly connected networks in area 0 using classless network addresses.
Set interface G0/0 as passive.
Step 3: Configure OSPF on R3
Configure OSPF on R3.
Advertise all directly connected networks in area 0 using classless network addresses.
Set interface G0/1 as passive.
Step 4: Configure OSPF on R4
Configure OSPF on R4.
Advertise all directly connected networks in area 0 using classless network addresses.
Set interface G0/0 as passive.

## Slide 15: OSPF Verification and Ping Testing Verify OSPF Configuration
1
Display the routing table on router R1.
(use the show ip route ospf command to display the routing table).

## Slide 16
2
From D1 Ping:
D2 (172.41.180.10)
D3 (180.20.180.10)
D4 (180.20.180.11)
D5 (180.20.180.12)

## Slide 17: Configure a Standard ACL on R4:
Step 1: Configure the Standard ACL
Allow devices on 172.40.180.0/24 to access 172.41.180.0/25 except D1 (172.40.180.10).
Allow 2 devices from 180.20.180.0/26 (pinged by D1) to access 172.41.180.0/25.
Permit other traffic on 172.41.180.0/25.
Use access list number 80.
Step 2: Apply the ACL
Apply to Router R3 interface G0/1 for exiting traffic.
Step 3: Test the ACL a) From D1 and two hosts on 180.20.180.0/26, ping D2 (should not succeed from D1). b) Change D1’s IP to 172.40.180.20, then ping D2 (should succeed only for D1).

## Slide 18: Summary project aims to Enhance our practical skills in
security
network configuration

## Slide 19: Thank you
Do you have any questions ?